Rutherford Scattering Pre-lab Questions
Consider the difference in the Rutherford cross-section as a function of angle. If we able to measure four angle settings between 35° and 150°, which four angle settings would you choose to test the Rutherford cross-section formula? Please explain the reasoning for your choice.
The Rutherdford cross-section has a sin-4(θ/2) angle dependency. For values near 90°, the denominator diverges and the number of expected particles approaches 0. I would choose the two extremes and values close to the two extremes though slightly offset from each other. For example, four possible angles would be 35°, 40°, 140°, and 150°.

If the full-width at half maximum of the alpha peaks in the detector at 168° is about 0.1 MeV, at what incident beam energy will the peaks due to scattering from the gold and silver nuclei be separated by twice the peak resolution?

Since the scattering angle and target masses are the same, K is constant and to double the peal resolution we must double the incident energy.