Energy Dispersive X-ray Spectroscopy (EDXS)
What determines the ability of the EDXS to identify elemental composition of a material?
The incident particles excite and eject an electron from its energy shell. The electron hole is then filled by an electron in a higher orbital. The transition of the higher-energy electron to the lower-energy state releases an X-ray. The energy of the X-ray is dependent on the energy difference in the energy levels. Additionally, some samples have overlapping peaks and non-homogeneous samples can have problematic peak overlapping. Larger, denser samples will have less of a chance that an X-ray will escape the sample therefore will not be able to be detected.

It is challenging to measure the amount of light elements (such as H, He, Na, Be) in a sample using EDXS. Why?

Light elements only emit K rays. The gold layer and using a Beryllium window, low-energy X-rays are easily absorbed making the detection of light elements difficult.

References

[1]Wikipedia contributors. "Energy-dispersive X-ray spectroscopy." Wikipedia, The Free Encyclopedia.	Wikipedia, The Free Encyclopedia, 16 Feb. 2017. Web. 13 Mar. 2017.